## Slide 1: LoX and Ethanol Handling Training

## Slide 2: Introduction to LoX and Ethanol
This training will cover:
- Properties and hazards of LoX and Ethanol
- Safe handling procedures
- PPE requirements
- Emergency response protocols
- Equipment operation

## Slide 3: Properties and Hazards of Liquid Oxygen (LoX)
LoX is a cryogenic liquid with an extremely low boiling point (-183°C). It can cause severe burns and frostbite upon contact with skin. LoX can also cause materials to become highly flammable, leading to explosive reactions in the presence of fuel sources.

## Slide 4: Properties and Hazards of Ethanol
Ethanol is a flammable liquid with a flashpoint of 13°C. It can cause fires and explosions if not handled properly. Ethanol vapors can form explosive mixtures with air and should be stored and handled in well-ventilated areas.

## Slide 5: Safe Handling Procedures for LoX and Ethanol
When handling LoX:
- Always wear appropriate PPE
- Ensure proper ventilation to prevent oxygen enrichment
- Avoid contact with flammable materials
When handling Ethanol:
- Use spark-proof tools and equipment
- Ground and bond containers to prevent static discharge
- Store away from heat sources and open flames

## Slide 6: Personal Protective Equipment (PPE) Requirements
Required PPE for handling LoX:
- Cryogenic gloves
- Face shield
- Insulated boots
Required PPE for handling Ethanol:
- Flame-resistant clothing
- Chemical-resistant gloves
- Safety goggles or face shield

## Slide 7: Emergency Response Protocols
In the event of a LoX spill:
- Evacuate the area immediately
- Ventilate the area to disperse oxygen-enriched air
- Use proper spill kits to contain and clean up the spill
In the event of an Ethanol spill:
- Remove all ignition sources
- Evacuate the area and ventilate
- Use foam or dry chemical extinguishers to control fire