## Slide 1
INNOVATIVE SPACE CARRIER - EXOS
ASCA ETV
EXPERIMENTAL TRAINING VEHICLE
MARCH, 2026
EXOS AEROSPACE
EXOS AEROSPACE | www.exosaero.com | CONFIDENTIAL 1

## Slide 2
ASCA 1.0
Flight altitude: 0.1 km (328ft) ・Purpose: Demonstration of vertical takeoff and landing ・Features: - Hadley engines (2?) - ~40% of the airframe mass
3D-printed - Adoption of Model Predictive
Control (MPC) for powered
landing - Autonomous flight safety measures
- Spaceport America (NM, USA)
ASCA ETV (Experimental Training Vehicle) Goals
  Multiple VTVL missions to demonstrate reusability and repeatability.
  Performance evaluation for subsystems and components.
  Replacing various components to evaluate
EXOS AEROSPACE
2 / 15
EXOS AEROSPACE | www.exosaero.com | CONFIDENTIAL

## Slide 3
  Designed, fabricated and test flown by today’s EXOS team, then Armadillo Aerospace in 2010 (old construction technology)
  From concept to successful flight test at our Caddo Mills test center in four months.
  LOX/Ethanol propulsion and stowable/deployable landing legs
  This video shows a “boosted hop”, engine always on, to 1,200m with a precision landing dead center of the launch pad.
SuperMOD VTVL
EXOS AEROSPACE
3 / 15
EXOS AEROSPACE | www.exosaero.com | CONFIDENTIAL

## Slide 4
Designed for USAF/AFRL to test new Rotating Detonation Propulsion Technology.
Currently under construction with test flights scheduled in 2026Q3.
USAF/AFRL opted initially for hover testing only not VTVL boosted hops.
Currently reviewing an extension program to take the HVRR RDRE to free flights.
This vehicle is capable of VTVL boosted hops with precision landing to ~20km+
High altitude hops can be undertaken under FAA AST regulations, 14CFR §437 “Experimental Rocket Testing” or §101 waiver.
No 14CFR §450 Launch License required
EXOS HVRR RDRE
EXOS AEROSPACE
4 / 15
EXOS AEROSPACE | www.exosaero.com | CONFIDENTIAL

## Slide 5
EXOS BLK3 PRSLV
  Precision Reusable Suborbital Launch Vehicle
  Designed, built & successfully static / hover tested for USAF in 9-months
  Constructed using EXOS-SSLC all Carbon Fiber Composite [CFC]
  Type V cryogenic (LOX) compatible, TRL9 space-rated, propellant tanks with integral structure (the tanks are part of the airframe.)
  Two-stage recovery, with supersonic decelerator ballute and GPS guided Joint Precision Air Drop System [JPADS] main chute.
EXOS AEROSPACE
5 / 15
EXOS AEROSPACE | www.exosaero.com | CONFIDENTIAL

## Slide 6
EXOS SCOPE OF SUPPLY
Hosokuni san [ISC] would like to hear about what kinds of systems & technologies your company (EXOS) has available.
Propulsion Module
  LOX/Ethanol engines (6kN/1,350lbf – 25kN/5,700lbf MSL)
  Simple, robust, pressure-fed (no turbopump!) & film-cooled chambers.
  Designed for reusability (clean running) & multiple restarts in flight.
  One man-rated flight engine demonstrated 1,000 successive relights.
  Throttleable down to 30% thrust & stable combustion.
  Simple design drastically reduces part count compared to other engines in the same thrust class.
  Engine is gimbaled using gear driven actuators for precise GNC.
  Dual, linked propellant valves with Main Propellant Feed [MPF] and inline Master Cut-Off [MCO] valves as part of the Flight Safety System.
  Thrust Termination System [TTS] back up to Main Flight Computer
EXOS AEROSPACE
6 / 15
EXOS AEROSPACE | www.exosaero.com | CONFIDENTIAL

## Slide 7
EXOS SCOPE OF SUPPLY
Propellant Tanks (LOX & Ethanol or RP)
  All EXOS-SSLC Carbon Fiber Composite [CFC] technology.
  Linerless, out of autoclave cured construction. NOT 3D printed!
  US company (Relativity Space) abandoned 3D after launch failures.
  Type V, LOX compatible construction, particle and NVR cleaned to NASA specifications.
  TRL9 space-rated by NASA & SpaceX (tanks now on lunar surface)
  Tanks are part of the airframe; NOT tank within an airframe.
  Fore and aft “skirts” allow nesting of modules which increases structural strength & resistance to bending loads (Q-Alpha)
  Integral, CFC flanged connections.
  EXOS-SSLC CFC technology reduces parts count and dry mass.
  Changing from aluminum construction to CFC increased propellant capacity of the BLK3 by 50% and still reduced dry mass by ~30%
EXOS AEROSPACE
7 / 15
EXOS AEROSPACE | www.exosaero.com | CONFIDENTIAL

## Slide 8
EXOS SCOPE OF SUPPLY
Pressurant Module (Helium)
  All Carbon Fiber Composite CFC construction helium tank.
  Two designs
    Tank within an airframe
    Tank with integral structure (best for smaller launch vehicles)
  High pressure helium, 35MPa/5,000psig with 2.0 Safety Factor.
  Pressure regulation system with independent feeds to fuel and LOX tanks.
  Reduces bulk helium pressure to 2.75MPa/400psig.
  Pressurant module airframe (or tank) equipped with nesting skirts to slide inside other modules.
EXOS AEROSPACE
8 / 15
EXOS AEROSPACE | www.exosaero.com | CONFIDENTIAL

## Slide 9
EXOS SCOPE OF SUPPLY
Computer Module
  Carbon Fiber Composite [CFC] airframe
  Computer stack with Main Flight Computer [MFC] that provides autonomous, Guidance, Navigation & Control.
  JAVAD GNSS unrestricted GPS, multiple satellite system tracker for increased accuracy.
  Systron Donner IMU with Fiber Optic Gyros, Tactical Grade Inertial Navigation System.
  Sends signal to independent Watchdog Computer [WDC] so in event of MFC failure, WDC can terminate thrust.
  FAA AST 14CFR §437 launch license safety system compliant.
  Flight software is EXOS proprietary based on NASA Project Morpheus (lunar lander) software. (EXOS team built Morpheus)
EXOS AEROSPACE
9 / 15
EXOS AEROSPACE | www.exosaero.com | CONFIDENTIAL

## Slide 10
EXOS SCOPE OF SUPPLY
Recovery Module
  Although intended recovery is by powered landing, would recommend EXOS recovery system as back-up.
  Two-stage recovery system, 100km altitude capable.
  Supersonic Ballute decelerator, deployed at 30km+AGL & Mach 4
  Joint Precision Air Drop System [JPADS] GPS guided and steerable chute to land back at launch site., deployed at 3km AGL & 70m/s.
EXOS AEROSPACE
10 / 15
EXOS AEROSPACE | www.exosaero.com | CONFIDENTIAL

## Slide 11
EXOS SCOPE OF SUPPLY
Flight Testing
  EXOS can provide all ground launch control equipment and personnel to conduct missions and train ISC.
  Low altitude missions to ~1,200m can be undertaken at EXOS’ Caddo Mills Test Facility.
  Higher altitude flights to 20km – 100km to be undertaken at Spaceport America and/or other emerging test sites.
  EXOS can obtain 14CFR §437 Experimental Permit or §101 waivers as necessary for all the above missions.
  After training missions in the USA, EXOS can apply for 12CFR §123 “License for the Export and Temporary Import of Defense Articles.” to enable ISC to test in Japan.
  EXOS can assist ISC with license to conduct test missions in Japan (Hokkaido Spaceport?)
EXOS AEROSPACE
11 / 15
EXOS AEROSPACE | www.exosaero.com | CONFIDENTIAL

## Slide 12
PROPOSED EXPERIMENTAL TEST VEHICLES [ETVs]
HVRR VARIANT
Most similar to original ASCA 1.0 but significantly better performance.
Use proven EXOS LOX-Ethanol propulsion instead of experimental RDRE.
Add stowable / deployable landing legs for precision powered landings.
Add deployable CG shift module to allow freefall descent before engine relight.
Add EXOS two-stage recovery system for emergency recovery in event of system failure.
Multiple mission campaigns up to 20km at Spaceport America & in Japan.
~$3.0M and 12-months to free flights
EXOS AEROSPACE
12 / 15
EXOS AEROSPACE | www.exosaero.com | CONFIDENTIAL

## Slide 13
PROPOSED EXPERIMENTAL TEST VEHICLES [ETVs]
BLK3 VARIANT
More representative missions for booster recovery of orbital rocket
Add stowable/deployable legs for precision powered landing.
Add CG shift module for freefall guidance (grid fins?)
BLK3 already has EXOS two-stage emergency recovery system
Also has upper and lower cold gas Attitude Control System [ACS]
Multiple mission campaigns at Spaceport America & in Japan.
Following test campaign, BLK3 can be repurposed as Japanese Suborbital Zero-G launch vehicle; ~$1.0M per full manifest.
~$4.5M and 18.months to free flights.
EXOS AEROSPACE
13 / 15
EXOS AEROSPACE | www.exosaero.com | CONFIDENTIAL

## Slide 14
ISC FUTURE VISION – SSTO PASSENGER TRANSPORT
SSTO Passenger & cargo to LEO.
Glide body horizontal landing.
Point to Point [PtP] transportation globally in hours
Reusable aircraft like flight cadence & flight safety.
SSTO VERY difficult even with advanced propulsion & modern CFC technology.
Glide body recovery with delta wing & horizontal landing with retractable undercarriage (Shuttle like) is virtually impossible (mass fraction!)
Better solution would be recoverable/reusable first stage booster and glide body second stage horizontal recovery.
EXOS AEROSPACE
14 / 15
EXOS AEROSPACE | www.exosaero.com | CONFIDENTIAL

## Slide 15
EXOS AEROSPACE
THANK YOU
www.exosaero.com | jquinn@exosaero.com | +1-972-740-8355
Exos Aerospace Systems & Technologies, Inc.
EXOS AEROSPACE | www.exosaero.com | CONFIDENTIAL 15